Xen on Cubietruck
Bamvor Jian Zhang
Software Engineer
bjzhang@suse.com

---
Agenda
cubietruck
Arm virtualization extension
Xen on arm
demo

---
Arm SOC working by xen
- The arm32 port:
  - The Cortex A15 Real-time System Model's provided by ARM.
  - A Cortex-A15 Processor running on the Versatile Express.
  - The Arndale board.
  - The Calxeda ECX-2000 (aka Midway) server.
    - ARM in the server room faces a set back as Calxeda shuts down
  - Allwinner A20/A30 boards.
  - Google Chromebook.(in process)
- The arm64 port
  - Model
    - The AEMv8 Real-time System Models by ARM.
    - ARM v8 Foundation Model.(in process)
  - APM "Mustang". See TBD.

---
Ct: dual-A7, 2G memory, 1000M, SATA

---
Xen architecture

---
Arm virtualization
Hyp mode

---
Xen arm boot requirement(arm32)
- Boot in hyp mode
- Device tree
  - Pass by r2 register, or
  - Append at the end of xen zImage

---
U-boot: TODO: details
- Hyp patch: upstreamed
- Board support patch for hyp
- Enable arm generic timer for xen

---
Port my board to xen
- Cpu: Cortex-A7. Upstreamed
- Serial: synopsys IP. Upstreamed
- SMP: work in process.

---
Know issue
- Dom0 1:1 work around. Ref.
- Dom0 config auto generation.
- How to use the memory large r than 4G in arm32?
  - [Xen-devel] [PATCH v2] xen: arm: improve handling of system with non-contiguous RAM region
- Migration would be merged at xen 4.5.

---
Xen dom0 kernel
- At least kernel 3.8.
  - Compatablity?
- enable xen backend driver.

---
Xen domU kernel
- At least kernel 3.8.
  - Compatablity?
- enable xen frontend driver.

---
Wiki and my work tree
- http://wiki.xen.org/wiki/Xen_ARMv7_with_Virtualization_Extensions/Allwinner
- https://github.com/bjzhang/u-boot-sunxi
- https://github.com/bjzhang/linux-allwinner

---
Demo

---
Q & A

---
Arm virtualizaiton extension
	arm	x86
mmu
interrupt
timer

---
Exception offset	Exception (except monitor exception)	Operating modes	“正常”的异常
0x00	Reset	Supervisor	Software reset
0x04	Undefined Instruction	Undefined	Kgdb break inst
0x08	Supervisor Call (SVC)	Supervisor	Enter kernel space
0x0C	Prefetch Abort	Abort	Break inst
0x10	Data Abort	Abort	Page fault
0x14	Not used	-	-
0x18	IRQ (interrupt)	Interrupt	-
0x1C	FIQ (fast interrupt)	Fast interrupt	-

---
Problem and issue

---
- 1), 1:1 work around.
- dom0 1:1 map and system MMU?
- is dom0 1:1 map a work around?
- DMA

---
Gic base address is fix in currrent xen

---
Background

---
reference
http://www.linaro.org/documents/download/d7fe510d8eb46775afc3953d217b15224fbb93086598a